On the first page (pictures) :
The connector is indeed the receptacle with male contacts. In other words, the corresponding P/N are :
Connector (receptacle) : CEV1695-0001-A0001
Male contact : DEVS24609-0003 or DEVS24610-0003 (depending on wire diameter)

Second page :
This is the plug connector (that mates with the receptacle)
Therefore, since you are using a receptacle with male contacts, you need to use this plug with female contacts. Corresponding P/N are :
Connector (Plug 90°) : CEV1695-0063-A0001
Female Contact : DEVS24612-0003 or DEVS24613-0003 (depending on wire diameter)

Third page :
The contacts have to be chosen in accordance with the wire you will be using. Depending on the size (mm2) of the wire : diameter or width of the cable (width = cross section)

In order to seal the wires into the contacts, you need to crimp the contacts over the wires. For that purpose, you will have to use a “crimping” tool (plier) along with its positionner. The appropriate tool has the following P/N : OUT0405-0167AS0 and OUTS1695-0004.
Also, in order to insert the contact (when crimped over the wire) into the connector it is better to use an “insertion” tool to help the contact fit in the connector (OUTS1695-0003).
On the other end, if you need to remove a contact from the connector, you must use the corresponding “extraction” tool (OUTS1695-0002)
The other Plier (OUT0405-0223AS) which includes its positioner, needs to be used for crimping the ground contact (which is bigger than the DEVS contacts).
Basically, if you are not tooled up, you must get them too.